EVR ATA CONFIGURATION MANUAL

Abisai Ngalande

# Features and Description.
Feature	Description	Comment
Reset	If pressed briefly it will reboot the ATA. Press and hold it will reset the device to factory default
Phone 1 / Phone 2	Using an RJ-11 phone cable connect to either one or both ports, connect to an analog phone.
Ethernet (Yellow)	Connect to computer, or the local network using Ethernet cable.
Internet (Blue)	Connect to a broadband network, or a route network.
DC 5VPower	Connect 5V power source using the right cable

# Connections
1. Connect an analog phone to port 1.
2. Connect computer to Ethernet port using Ethernet cable.
3. Connect another Ethernet to the internet port and to the network on the other side
4. Connect power cable.

# Configuration
The computer will get an IP address from ATA, which will be 192.168.15.0 network.
1. Log in the ATA using 192.168.15.1 through browser, this is default IP address.
2. Enter username and password as admin
# Entering connection details
## Select Quick Setup
Line 1
1. Proxy = 192.168.84.3
2. Display Name = “Village name”
3. Password = Mtema01
Line 2
Enter the same details as line 1
## Click on Network Service Tab
1. Click on a drop down menu and select “BRIDGE”
2. Click submit to save
## Network Settings
Select static and enter
  - IP address 192.168.100.5
  - Netmask 255.255.255.0
  - Gateway 192.168.100.1
  - Host name “village’s name”
Submit
Done