Hardware Installation SoP

Abisai Ngalande

# 1.0 Applicability
This SoP describes the operation, function, and guide line of hardware installation in site where baobab systems will be used.
## 1.1 Users
It is to be used by installation and support officers and quality assurance team.
# 2.0 Safety
All the officers must understand the hazards related to electrical installation and all that build safety.
## 2.1 Improper usage
Failure to use this will lead to poor quality out look of the site, and poor performance of the system.
# 3.0 Coverage of the SoP.
This document will provide guide lines on
- Power installations
- Network installation
## 3.1.0 Power Cabinet
The power cabinet is the unit which handles all the power related gadgets. It is one of the most important unit in the installation. This needs to be installed in a secured and centralized place. It is recommended that the server cabinet be installed in the same area.
Power cabinet house the following items:-
- Main switch
- AC Circuit breaker
- Twin surface socket
- Automatic Voltage Switch (AVS)
- Battery charger, this can be 48V or 24V depending on the system.
- DC circuit breakers
- Low voltage disconnect
- Batteries
- Cooling Fans
### 3.1.1 Function of Items
### 3.1.1.0 Main switch
The main switch is installed to protect when there	is earth leakage over current drawing.
Feed cable should be connected from the building main feed to the main switch in the cabinet. Connect the feed behind the main switch of the building so that there is no disturbance on the response.

### 3.1.1.1 Ac circuit breaker