Casing
Position of the holes
Number of holes
Hole spacing
Size of the holes
Position of the board
Cables
length of the input cable
Length of the output
Output cable specification

Soldering
Quality Check-list
- Heat sink
- Heat paste
- Silicon
- Tape
- LED
- Strain relief
- Terminal cut outs
- Polarity

Parts List
R1- NA
R2-39K
R3-3.3K
R4-2.2K
R5-33K
R6-3.9K
R7-2.2K

C1-4700/35V
C2-2200/63V
C3-103
C4
C5
C6
C7

IC1-LT1074HV

D1-8TQ100
D2-8TQ100

L1-2200LL-680-H-RC

J2 power supply modification

Input voltage range.

To increase the input voltage range we need to change the value of R2 and R3 to 19k (we use 18K) and 2.4k respectively.

Input voltage	R2	R3
20V Minimum	18k	2.4k

Output voltage

To adjust the output voltage we need to change the value of R5 and R6

Out Voltage	R5	R6
28.2	33k	2.7k
16.7	25k	3.9k
12.2	18k	3.9k
5.1	5.1k	3.9k
3.35	3K	5.6K